## Slide 1
Finite Element Analysis (FEA) Lab Project 2025
Structural Analysis of a Hexagonal Component
Muhammad Anus (ME-1865)
Section A | Semester 7th | National University of Sciences & Technology

## Slide 2
Project Objective
This project performs a comprehensive Finite Element Analysis (FEA) on a custom hexagonal component to evaluate its mechanical integrity under specific loading conditions.
Analysis Phases
The study encompasses two primary phases:
1.
Static Structural: Steady-state response to fixed loading.
2.
Transient Structural: Time-dependent response to variable loading.
Project Overview

## Slide 3
The material properties were defined using a custom configuration derived from the student's roll number (ME-1865).
Property | Value | Unit
Young's Modulus | 65,000 | MPa
Poisson's Ratio | 0.28 | -
Tensile Yield Strength | 300 | MPa
Bulk Modulus | 4.92 × 104 | MPa
Material Properties

## Slide 4
To ensure simulation accuracy, a rigorous meshing strategy was employed:
Element Type: Utilized Hex20 (20-node brick elements), known for high-order accuracy in 3D structural problems.
Face Meshing: Explicitly applied to faces 2 through 7 to force a structured grid.
Quality Metrics: The mesh metrics confirmed excellent element quality, with values predominantly close to 1.00, ensuring solution stability.
Meshing Strategy

## Slide 5
Boundary Conditions
Solver Settings
Fixed Support: Applied to one face of the hexagonal component, constraining all degrees of freedom (DOF) to simulate a rigid mount.
Remote Force: A calculated force of roughly 2061 N was applied to the opposing face to induce mechanical stress.
Convergence: The solution was configured for up to 10 loops but achieved rapid convergence within just 3 steps.
Stability: The minimal change (2.35e-10%) between final steps indicates a highly stable numerical solution.
Static Analysis Setup

## Slide 6
Static Analysis Setup

## Slide 7
Static Results: Stress & Convergence
Equivalent (Von-Mises) Stress
The simulation yielded a maximum stress of 107,300 Pa (0.107 MPa).
Safety Conclusion: The induced stress is significantly lower than the material's Tensile Yield Strength of 300 MPa.
The component is well within the elastic limit, showing no risk of plastic deformation or failure under the applied static load.

## Slide 8
Minimal Displacement
The maximum total deformation observed was:
This negligible value highlights the high stiffness of the material (E = 65 GPa) and confirms the structural rigidity of the design under the prescribed loading conditions.
Static Results: Deformation

## Slide 9
.
Load Label | Magnitude | Application Side
Force 1 (B) | 1,000 N | Upper-left
Force 2 (C) | 2,000 N | Right Side
Force 3 (D) | 3,000 N | Lower-right
Force 4 (E) | 4,000 N | Bottom-left
Transient Analysis Setup

## Slide 10
Max Stress
7.769 × 10 5 Pa
(0.78 MPa)
Increased due to multiple simultaneous loads.
Max Deformation
3.088 × 10 - 7 mm
(Transient Peak)
Higher than static but still negligible.
Transient Results

## Slide 11
Transient Results

## Slide 12
"The FEA simulation confirms the structural integrity of the hexagonal component. Under both static and transient loading conditions, the induced stresses are well below the yield strength, ensuring a high factor of safety."
“
Conclusion

## Slide 13
Thankyou 